## Slide 1
Glider Workshop
UCF SECME Glider Competition 2023-2024
Chris Stevens, Dr. Michael Kinzel

## Slide 2
What makes a good glider?
  Wing Shape
  The Importance of a Tail
  Balance
Competition Rules
What Makes a Good Glider?

## Slide 3
Long, Thin Wings
  Length/Chord ratio >6
  Maximum Lift/Drag in slow flight
Wing Design
Smooth, Thin Airfoil Shape
  Essential for good gliding performance
Wing Length
Wing Chord
Wing Span

## Slide 4
Swept Wings, Bad Idea for Gliders
  Doesn’t help at low speeds
  Makes structure difficult/heavy
Wing Design
Dihedral Angle
  Stabilizes straight forward flight
  Slightly decreases lift
  Can be polyhedral (flat and angled)

## Slide 5
Wings must be strong enough
  Light, but strong design
  The more bend, the less lift
Wing Structure
Example wing structure
  Folded material with spar
Leading (front) Edge
Trailing (back) Edge
Spar (structural support)

## Slide 6
Tail is critical for stability
Horizontal Stabilizer
  At least 1/5 area of wings
Vertical Stabilizer
  At least 1/10 area of wings
Fuselage Length
  4-6x wing chord length
  If too short, won’t be stable
Tail Design
Vertical Stabilizer
Horizontal Stabilizer
Fuselage Length
Chord Length
Canards and Flying Wings
  More efficient
  Almost always unstable

## Slide 7
Forces on a glider
Gravity
Drag
Lift
Thrust?
Gravity
Stabilizer Lift
Drag
Lift

## Slide 8
Balance
Short (1/4 of body length)
Long (3/4 of body length)
Center of Lift, at ~1/4 cord length
Center of Gravity (balance point)
Wingspan
Most important, Center of Gravity (with marbles) in front of Center of Lift
  Center of Gravity (where you balance the weight)
  Center of lift (center of the wing and horz tail)
  CG too far forward flies poorly, CG too far back flies once
Body length should be close to wingspan
  Back section 4-6x Wing Cord Length

## Slide 9
Wrap-Up
Long, thin wings. Strong enough to hold up
Tail Surfaces
  Far enough back, big enough to keep the plane stable
  Lightweight
Balance
  Center of Gravity (where you balance the weight) before Center of lift (center of the wing and horz tail)

## Slide 10
Rules Review
Minimum 24in Wingspan, no max
Maximum 4x4 Body Width, any length
Must carry 16 marbles in sealed sandwich bag, 2.1oz
Weight between 8oz and 12oz (including marbles)
Total of 4 flights, score is total distance glided
If glider breaks, score reduced by 25%
No designs/parts from kits, no metals/hard materials for safety

## Slide 11
Suggestions
Hobby/craft stores have balsa wood, foam board, monokote/ultracoat
  Dollar Tree is good place for foam board (~$1)
Leading edge balsa wood is great
You can build small balsa gliders for practice
Don’t waste material/weight on unnecessary things

## Slide 12
Wrap-Up
  Good luck!
  If you have any questions, you can contact us at AIAA.Central.FL@gmail.com