## Slide 1
Glider Workshop
UCF MISSION: STEM Glider Competition 2024-2025
Rhett Jefferies, PhD

## Slide 2
What makes a good glider?
  Wing Design
  The Importance of a Tail
  Balance
Competition Rules
What Makes a Good Glider?

## Slide 3
Long, Thin Wings
  Length/Cord ratio >6
  Maximum Lift/Drag in slow flight
Wing Design
Smooth, Thin Airfoil Shape
  Essential for good gliding performance
Wing Length
Wing Chord
Wing Camber

## Slide 4
Swept Wings, Bad Idea for Gliders
  Doesn’t help at low speeds
  Makes structure difficult/heavy
Wing Design
Dihedral Angle
  Stabilizes straight forward flight
  Slightly decreases lift
  Can be polyhedral (flat and angled)
Wing Span

## Slide 5
Wing Structure
  Light, but strong design
  The more bend, the less lift
Wing Design
Example wing structure
  Folded material with spar
Leading (front) Edge
Trailing (back) Edge
Spar (structural support)

## Slide 6
Tail is critical for stability
Horizontal Stabilizer
  At least 1/5 area of wings
Vertical Stabilizer
  At least 1/10 area of wings
Fuselage Length
  4-6x wing chord length
  If too short, won’t be stable
Tail Design
Vertical Stabilizer
Horizontal Stabilizer
Fuselage Length
Cord Length
Canards & Flying Wings
  More efficient
  Almost always unstable

## Slide 7
Forces on a glider
Gravity
Drag
Lift
Thrust?
Gravity
Stabilizer Lift
Drag
Lift

## Slide 8
Most important, Center of Gravity in front of Center of Lift
  Center of Gravity (CG) too far forward flies poorly; CG too far back flies once
Fuselage (Body) length should be close to wing length
Glider Balance
Short (1/4 of body length)
Long (3/4 of body length)
Center of Lift ~1/4 chord length
Center of Gravity (balance point)
Wingspan

## Slide 9
Design Summary
Long, thin wings. Strong enough to hold up
Tail Surfaces
  Far enough back, big enough to keep the plane stable
  Lightweight
Balance
  CG in front of center of lift

## Slide 10
Competition Rules
Minimum 24in Wingspan, no max
Maximum 4x4 Body Width, any length
Must carry 16 marbles in sealed sandwich bag, 2.1oz
Weight between 8oz and 12oz (including marbles)
Total of 4 flights, score is total distance glided
Obstacle, 2x2 milk crates 26x26” at 15 ft.
If glider breaks or hits obstacle, score reduced by 25% for flight
No designs/parts from kits, no metals/hard materials for safety

## Slide 11
Suggestions
Hobby/craft stores have balsa wood, foam board, monokote/ultracoat
Balsa wood for leading edge is great
Build a smaller version early to try out design & practice
Don’t waste material/weight on unnecessary things

## Slide 12
Wrap-Up
  Good luck!
  If you have any questions, you can contact me
  rhett.Jefferies@ucf.edu
  321-945-0786